## Slide 1: Photography

## Slide 2: Explain the principles of camera construction

## Slide 3
A pinhole camera is a simple camera without a lens but with a tiny aperture (the so-called pinhole)—effectively a light-proof box with a small hole in one side. Light from a scene passes through the aperture and projects an inverted image on the opposite side of the box, which is known as the camera obscura effect.

## Slide 4: What the camera lens does ?

## Slide 5
A camera lens usually has an aperture adjustment mechanism to control the amount of light that may pass. It also has a shutter, to control the length of time during which light may pass through the lens.

## Slide 6: The effect of light on light-sensitive film

## Slide 7
Photographic film is a sheet of plastic which is coated with an emulsion containing light-sensitive silver halide salts with variable crystal sizes that determine the sensitivity and resolution of the film. When the emulsion (in this film) is subjected to sufficient exposure to light it forms an invisible image.

## Slide 8: The action of developers

## Slide 9
In film developing, photographic developer (or just developer) is a chemical that makes the latent image on the film (or print) visible. It does this by reducing the silver halides that have been exposed to light to metals of elemental silver in the gelatine matrix. As a generalisation, the longer a developer is allowed to work, the greater the degree of reduction of the silver halide crystals to silver and therefore the darker the image.

## Slide 11: What is meant by the "speed” of the film

## Slide 12
Film speed is the measure of a photographic film's sensitivity to light. Stock with lower sensitivity (lower ISO speed rating) requires a longer exposure and is thus called a slow film, while stock with higher sensitivity (higher ISO speed rating) can shoot the same scene with a shorter exposure and is called a fast film.

## Slide 13: What does ASA/ISO mean?

## Slide 14
The standard known as ISO 5800:1987 from the International Organization for Standardization (ISO) defines both a linear scale and a logarithmic scale for measuring film speed.
In the ISO linear scale, which corresponds to the older ASA scale, doubling the speed of a film (that is, halving the amount of light that is necessary to expose the film) implies doubling the numeric value that designates the film speed. In the ISO logarithmic scale, which corresponds to the older DIN scale, doubling the speed of a film implies adding 3° to the numeric value that designates the film speed. For example, a film rated ISO 200/24° is twice as sensitive as a film rated ISO 100/21°.

## Slide 15: How are shutter speed, lens aperture, and film speed related?

## Slide 16
Shutter speed is the time for which the shutter is held open during the taking of a photograph to allow light to reach the film or image sensor (in a digital camera). Combined with adjusting of the lens aperture, the shutter speed regulates how much light the camera will record.
Film speed is the measure of a photographic film's sensitivity to light.

## Slide 17: Give the principal uses of photography.

## Slide 18
Photography [fә'tɑgrәfi:],[foʊ'tɑgrәfi:] is the process of recording pictures by means of capturing light on a light-sensitive medium, such as a film or sensor. Light patterns reflected or emitted from objects expose a sensitive chemical or electronic medium during a timed exposure, usually through a photographic lens in a device known as a camera that also stores the resulting information chemically or electronically.

## Slide 19: Take print or slide pictures illustrating at least eight of the following techniques.

## Slide 20
Framing

## Slide 21
Camera steadiness

## Slide 22
Direction of lighting - front, backlighting, side

## Slide 23
Panning - background blurred
with subject in focus

## Slide 24
Rule of thirds

## Slide 25
Angle - high level

## Slide 26
Angle – eye level

## Slide 27
Angle - low angle

## Slide 28
Level horizon

## Slide 29
Fill the frame

## Slide 30
leading lines

## Slide 31
Quality of light

## Slide 32
Quality of light - shade

## Slide 33
Quality of light – Mid-Day

## Slide 34
Quality of light - Sunset

## Slide 35
Correct exposure - underexposed, overexposed, and correctly exposed

## Slide 36
Use of flash - distance
and reflective objects

## Slide 37
Use of flash - distance
and reflective objects

## Slide 38
Use of flash - distance
and reflective objects

## Slide 39
“You don’t take a photograph, you make it.”
Ansel Adams

## Slide 40
@LUILLI2700

## Slide 41
You made it!
thank you everyone